## Slide 1: Edge AI Threat-Sound Detection
Glass break · Scream · Normal
Raspberry Pi 4 · YAMNet · IoT alerts
Final presentation · June 22, 2026
HUFS IoT TERM PROJECT
REAL-TIME SMART SURVEILLANCE
Notes: Good afternoon. Our project is an edge AI security system that listens for two threat sounds: breaking glass and screams. It runs on a Raspberry Pi, classifies audio in real time, and triggers physical and remote alerts. I will focus on the baseline, our model, what failed, what finally worked, and what should improve next.

## Slide 2: Why listen for threats?
COVERAGE GAP
Cameras and motion sensors miss events outside their field of view. Sound adds an independent signal.
EDGE PRIVACY
Audio is analyzed locally on a Raspberry Pi. Only detected events and evidence are transmitted.
AUTOMATED RESPONSE
One detection triggers a buzzer, LED, camera capture, event log, and Telegram notification.
Notes: Why use sound at all? Cameras and motion sensors are useful, but they have blind spots. A microphone can detect an event even when the source is outside the camera view. Our design also keeps inference on the edge: raw audio does not need to be continuously uploaded. When a threat is confirmed, the system can immediately activate a buzzer and LED, take a photo, write a log, and send a Telegram message.

## Slide 3: Baseline: YAMNet-only ablation
16 kHz
Mono audio
waveform
YAMNet
Pretrained AudioSet
network
521
Generic class
probabilities
Rules
Map scores to
3 target classes
Exploratory post-hoc test ablation: Macro F1 0.756; glass recall 20/29; scream recall 19/38. Not used for model selection.

## Slide 4: Retained model: YAMNet embeddings + custom head
01
FRONT END
16 kHz mono audio enters frozen YAMNet. Each frame becomes a 1,024-dimensional embedding.
• pretrained features
• cached embeddings
• frame-level input
02
TASK HEAD
Dense 512 → 256 → 128 → 3-way softmax, with batch normalization, dropout, and L2 regularization.
• glass
• normal
• scream
03
OFFICIAL POLICY
Validation-selected classifier thresholds convert frame probabilities into one audio-level label.
• glass: 0.95 / 1 frame
• scream: 0.40 / 3 frames
• no YAMNet fusion
Notes: Our retained model keeps YAMNet as a frozen feature extractor but adds a task-specific classifier. Every audio frame becomes a 1,024-dimensional embedding. The classifier uses dense layers of 512, 256, and 128 units, followed by a three-class softmax. Batch normalization, dropout, and L2 regularization reduce overfitting. The official policy was selected on validation and uses classifier-only thresholds of 0.95 for glass and 0.40 for scream, with one and three consecutive frames respectively.

## Slide 5: A stricter experiment, not just a larger dataset
DATA QUALITY
We excluded 158 broad “smash / breaking / crushing” glass clips and kept only verified glass or shatter events.
LEAKAGE CONTROL
Splits were made by original source. Duplicate files and shared YouTube IDs cannot cross train, validation, and test.
SELECTION RULE
Candidates and thresholds use validation only. The 165-group test set is evaluated once after selection.
Train: 732 groups
Validation: 156 groups
Test: 165 groups
Seed: 42
325 duplicate aliases merged
Original-source split
No test threshold tuning
Independent groups
Validation promotion gate:
Macro F1 > retained model
Normal false alarm ≤ 5%
Both event recalls ≥ 70%

## Slide 6: Official test results
WHAT THE NUMBERS MEAN
The retained model recovered most glass events, but missed 11 of 38 screams and raised 13 alarms on 98 normal groups.
No candidate passed the validation promotion gate, so the operating model was not replaced.
13.3%
Normal false alarm · 13/98
82.8%
Glass recall · 24/29
71.1%
Scream recall · 27/38
165
Test groups
82.4%
Accuracy · 136/165
0.801
Macro F1
Notes: These are the official strict-label test results for the retained model. It correctly classified 136 of 165 source groups, for 82.4 percent accuracy and 0.801 Macro F1. Glass recall was 24 of 29, and scream recall was 27 of 38. On 98 normal groups, 13 produced a false alarm. These counts are important because the class sample sizes are modest. No new candidate passed the validation promotion rule, which required higher Macro F1 than the retained model, at most five percent normal false alarms, and at least seventy percent recall for both events.

## Slide 7: Trial and error changed the evaluation, not only the model
CANDIDATE C
Normal false alarms fell to 3.2%, but scream recall was only 60.5%. We rejected the upgrade.
FINAL SELECTION
BROAD LABELS
Generic breaking sounds polluted the glass class. We removed 158 unverified clips and rebuilt the split.
MIDTERM
DATA AUDIT
MEAN POOLING
A diagnostic example showed short impacts disappearing inside long averages. This was not an official accuracy result.

## Slide 8: Official vs. original demo
OFFICIAL
Classifier-only; thresholds 0.95 / 0.40; consecutive frames 1 / 3. Macro F1 0.801, normal false alarms 13.3%.
ORIGINAL DEMO
Classifier + YAMNet fusion; thresholds 0.97 / 0.92 plus scream mean and margin. Live loop also had an RMS gate.
TRADE-OFF
Offline ablation without RMS: Macro F1 0.804, false alarms 7.1%, glass recall 82.8%, scream recall 57.9%.
Notes: The official and original demo policies optimize different risks. The official classifier-only policy achieved Macro F1 0.801, normal false alarms of 13.3 percent, glass recall of 82.8 percent, and scream recall of 71.1 percent. The original demo used higher thresholds, YAMNet corroboration, scream mean and margin filters, and an RMS gate in the live microphone loop. The historical offline ablation did not include that RMS gate. In that ablation, Macro F1 was 0.804, false alarms fell to 7.1 percent, glass recall stayed at 82.8 percent, and scream recall fell to 57.9 percent. This comparison was not used for model selection.

## Slide 9: Where we can improve next
DATA
Collect more real microphone screams and hard negatives from the actual deployment environment.
MODEL
Fine-tune selected YAMNet layers or add a compact temporal model for event duration and context.
DEPLOYMENT
Benchmark the complete pipeline on Raspberry Pi and calibrate thresholds per microphone and room.
• room impulse augmentation
• impact / speech negatives
• label review workflow
• site-specific validation
• focal or cost-sensitive loss
• class-specific calibration
• temporal smoothing
• uncertainty rejection
• current: TF Hub + H5
• TFLite converts head only
• end-to-end latency
• false alarms per hour

## Slide 10: Security that listens
Transfer learning made the system practical
Source-group splitting reduced leakage risk
Validation gates prevented a risky upgrade
Official and demo policies expose a trade-off
Next: fewer false alarms without recall loss
Notes: To conclude, transfer learning made the detector practical, while source-group splitting and explicit validation gates made the evaluation more defensible. Comparing the official and original demo policies exposes the real trade-off: fewer false alarms versus more missed screams. The next engineering goal is to reduce false alarms without sacrificing threat recall. Thank you. I am ready for your questions.